## Slide 1: How to use Geometric Calibration of Micro-Lens-Based Light Field Cameras using Line Features
Yunsu Bok, Hae-Gon Jeon and In So Kweon
Robotics and Computer Vison Lab., KAIST
IEEE Transactions on Pattern Analysis and Machine Intelligence, Accepted

## Slide 2: Step 0 : LFP  raw (Lytro)
We use lfpsplitter to get raw image from the lfp file.
Download : https://github.com/nrpatel/lfptools
raw  png
Read 3280x3280 12-bit values from a raw file.
Then apply ‘demosaic’ algorithm in MATLAB
(sensor alignment: bggr)

## Slide 3: Step 0 : LFP  png (Lytro Illum)
We use the open source decoder “illum_full” made by Michael Tao,
a Ph.D student of UC Berkeley.
Source code available at : http://cseweb.ucsd.edu/~ravir/illum_full.zip
Set file format to Lytro RAW

## Slide 4: Step 1
Execute LightFieldCalib_Step1_MicroLensCenter.m
Drag and open White images

## Slide 5: Step 1
Set radius to 5 for a Lytro camera
Set radius to 7 for a Lytro Illum camera
Microlens radius is 7 pixels

## Slide 6: Step 1
Red dots are centers of microlens array.

## Slide 7: Step 2
Make pattern_size.txt file in image folder, and then input the size of pattern (unit: mm)

## Slide 8: Step 2
Move Microlens_center_list.mat in white images folder to pattern images folder

## Slide 9: Step 2
Execute LightFieldCalib_Step2_CenterImage.m
Drag and open Pattern images

## Slide 10: Step 2

## Slide 11: Step 3
Execute
LightFieldCalib_Step3_LineFeature
Drag and open Pattern images again

## Slide 12: Step 3

## Slide 13: Step 4
Execute LightFieldCalib_Step4_LinearSolution.m
Drag and open Lxxx.mat files

## Slide 14: Step 5 : Look-up table
Execute LightFieldCalib_Step5_LookupTable.m
open IntParamLF.mat files

## Slide 15: Step 6 : Sub-aperture image
If you want to detect corners of pattern images in sub-aperture image, DetectCorner =true
Otherwise, DetectCorner =false
Execute LightFieldCalib_Step6_SubApertureImage.m

## Slide 16: Step 6 : Sub-aperture image

## Slide 17: Step 6 : Sub-aperture image (Error Measure)
If you want to calculate projection Error and Ray reprojection error on checker board images, execute LightFieldCalib_Step6_SubApertureImage_ErrorAnalysis.m with lenslet images that you generate sub-aperture images. Please refer our TPAMI paper.

## Slide 18: Question
Please contact Ph.D Yunsu Bok
E-mail : ysbok@rcv.kaist.ac.kr